## Slide 1: Unsupervised Time Series Anomaly Detection Peter Chen
Notes: New R&D project that I recently started working on.
This project will have a lot of overlap with a masters project that I am doing for my Georgia tech master degree.

## Slide 2: Anomaly detection
Traditional Anomaly Detection for Machine Data
Tiered alarm systems using expert set thresholds and statistical analysis of data
Challenges
Lots of manpower needed to set thresholds
Lack of failure data - class imbalance
High Dimensional – difficult to visualize
Non-stationary – changing contexts (ex. Different ambient conditions)
  One size fits all thresholding technique is not ideal for non-stationary data
Potential Improvement
Unsupervised learning – Clustering/Autoencoders
  Learn to model nominal behavior
  Assess deviation for new data points to determine likelihood of anomaly
Notes: Background about Anomaly Detection for machine and manufacturing data
Traditionally, Anomaly detection has been done with thresholding techniques that are tuned by domain experts and statistical analysis of data
Potential improvement is to use unsupervised learning – get a good model of nominal/non-failure behavior
Use this model to assess deviation from nominal behavior to classify data as an anomaly

## Slide 3: Neural Network Autoencoders
Symmetric neural network where inputs = outputs
Encoder – Decoder system with a middle bottleneck layer for dimension reduction
Goal – Learn the intrinsic structure of the data by prioritizing the important information (code)
Key Assumption: Structure is different for nominal data vs anomalous data
  Reconstruction error for anomalous data will be higher
Example Use Case
Autoencoder structure
bottleneck
784
10
784
Notes: One way to do this is using Neural Network autoencoders
Its an artificial neural network where the input data is identical to the output data.
Encoder - maps the inputs into a lower dimensional code
Decoder – aims to maps that encoding back into the original input with minimum error
Goal – learn the important information which represents the intrinsic structure in the data (code)

## Slide 4: Open Source Dataset #1: Paper Mill Machine Sensors
https://arxiv.org/pdf/1809.10717.pdf
Data: Time series of paper mill machine with 60 sensor parameters and 1 binary target variable indicating failures
  Failures represent when the machine breaks, breaks can take over 1 hour to resolve
Variables: Large class imbalance – 124 failure vs 18,274 non-failure points (failures in red)
Benchmark: In the paper, the best supervised model (XGBoost) had F1 score of .11
Sensor 3 out of 61
Notes: The first thing I did was to find an open source dataset to try this model on.
Machine sensor data
Time series
Labeled failures with high class imbalance
Paper mill dataset where failures represent breakages
Large class imbalance
Best model had f1 score of .11

## Slide 5: Autoencoder for Paper Mill
Dense
(32 units)
Dense
(16 units)
Input – 61 sensors
Dense
(32 units)
bottleneck
Anomaly Detection Method
Train model on non-failure data
  X = sensor inputs, y = sensor inputs
Set statistical threshold for nominal behavior based on training data's reconstruction error
  try 3 sigma, 5 sigma, and max threshold
Predict on test data
Calculate reconstruction error for test data
Classify anomaly based on error threshold
Output – 61 sensors
Notes: Left – network for the autoencoder
Right is the steps for anomaly detection
Train on non-failure data
Assess the reconstruction error of the training data to set a threshold for what normal behavior looks like
Predict on the test data and classify anomalies based on this threshold

## Slide 6
Data Preprocessing – Autoencoder
CSV file
Drop non-sensor variables
Binary target variable padding
Standard scaler
Train/test split
Allow for early prediction intervals
Train = 90% of non-failures
Test = 10% of non-failures and 100% of failures

## Slide 7: Preliminary Results
Autoencoder weights – 5K params
Failure – early interval = 1
Non failures
Training time = 1 second per epoch
Loss Curve
Failure – early interval = 2
Reconstruction Error
Early interval = 1 shows better separation of failures
Notes: Preliminary results
Model converges decently
Histogram of reconstruction error – red = failures and blue is non failures
  Top graph is early interval of 1 which means predicting one timepoint before failure

## Slide 8: Comparison to XGBoost
 | XGBoost (Paper) | 3σ threshold | 5σ threshold
Topology | NA | 32-16-32 | 32-16-32
Precision | .51 | .554 | .84
Recall | .07 | .303 | .218
F1 Score | .11 | .391 | .347
ROC AUC | Not provided | .70 | 
Thresholds calculated based on training data – 3 and 5 sigma
Perform classification based on threshold
Early prediction interval = 1
Test Residuals
Threshold 3s
Failures
Autoencoders handles class imbalance better than XGB for this dataset
Notes: How our model compares to XGBoost to predict failures 1 timestep before.
We assessed 2 thresholds for an anomaly – 3 sigma and 5 sigma and we found that overall our model performs significantly better
Its a very difficult dataset to predict failures but our model was able to have a higher precision, recall, f1 score with a roc auc of .70

## Slide 9: Residual distribution vs early prediction interval
Non
failures
Early = 1
Early = 2
Early = 3
Early = 4
Autoencoder’s capability deteriorates as early interval increases
 | Early 1 | Early 2 | Early 3
Topology | 32-16-32 | 32-16-32 | 32-16-32
Precision | .554 | .293 | .216
Recall | .303 | .98 | .065
F1 Score | .391 | .147 | .1
ROC AUC | .70 | .60 | .60
Early = 5
Error distribution for early intervals
Notes: Look at how far in advance our model can predict the anomaly.
On the left we have a boxplot where the y axis is reconstruction error and the x axis represents the early interval for our predictions.
We want the failures to stand out from the non-failures – and you can see for an early interval of 1 we have some distinct differences. And this corresponds to an AUC of .7
As we increase our early interval, our predictive capability goes down which is expected for the most part.

## Slide 10: Next Steps
Paper mill dataset
Assess different topologies, feature set
Apply rolling mean before anomaly detection
Benchmark K-means clustering method
Visualize failures vs non-failures with T-SNE
Find Other Datasets
Benchmark against other datasets
Develop code base for reuse
Assess LSTM for anomaly detection
Find other ways to assess reconstruction errors
Apply to UTC use case